## Slide 1
IoT Air Quality Monitoring System
Real-Time Air Quality Monitoring with ML Predictions

## Slide 2
Abstract
The IoT Air Quality Monitoring System is a comprehensive solution that combines Internet of Things (IoT) sensors, machine learning algorithms, and web-based visualization to provide real-time air quality monitoring and predictions.
The system uses ESP32 microcontroller integrated with DHT22 (temperature/humidity) and MQ-135 (air quality) sensors to continuously monitor environmental conditions. The collected data is transmitted to a Flask-based web server that processes it through an ensemble machine learning model achieving 81.66% accuracy (R² score).
The web dashboard provides real-time AQI (Air Quality Index) display, 6-hour forecasting, historical data analysis, multi-device management, and automated alert systems. The platform supports multiple users with secure authentication and includes production-ready features like automated backups, rate limiting, and comprehensive logging.
This system is ideal for homes, offices, industries, healthcare facilities, and educational institutions requiring continuous air quality monitoring with predictive capabilities.

## Slide 3
System Architecture
Hardware Layer: ESP32 + DHT22 + MQ-135 sensors
Communication: WiFi/HTTP data transmission
Backend Server: Flask + SQLAlchemy + ML Model
Machine Learning: Ensemble model (RF + GBM + SVR + Ridge)
Database: SQLite with automated backups
Frontend: Responsive web dashboard (HTML/CSS/JS)
Services: Email alerts, rate limiting, logging

## Slide 4
Key Features - Part 1
🌐 Real-Time Monitoring
Live AQI updates every 5 seconds with color-coded status indicators
🤖 Machine Learning
81.66% accuracy ensemble model with 23 engineered features
📊 6-Hour Forecasting
Predictive analytics for future air quality trends
📱 Responsive Dashboard
Modern web interface optimized for desktop, tablet, and mobile
🔐 User Authentication
Secure login system with password hashing and session management
💾 Data Storage
SQLite database with unlimited historical data retention

## Slide 5
Key Features - Part 2
⚠️ Alert System
Automated alerts with email notifications and buzzer warnings
📈 Trend Analysis
Improving/worsening/stable trend detection algorithms
🔍 Anomaly Detection
Real-time identification of unusual air quality patterns
📥 Data Export
Download historical data in CSV format for further analysis
🛠️ Admin Panel
System management with backup, cleanup, and optimization tools
🚀 Production Ready
Rate limiting, logging, automated backups, and validation

## Slide 6
System Requirements
Hardware Requirements
• ESP32 Development Board
• DHT22 Temperature/Humidity Sensor
• MQ-135 Air Quality Sensor
• Buzzer (optional for alerts)
• USB Cable for programming
• Breadboard and jumper wires
• 5V Power supply
Software Requirements
• Python 3.10 or higher
• Flask web framework
• SQLite database
• scikit-learn (ML library)
• pandas & numpy (data processing)
• Arduino IDE (for ESP32)
• Modern web browser
• WiFi network connection

## Slide 7
Real-World Applications
🏠 Home Automation
Monitor indoor air quality, automate ventilation systems, ensure healthy living environment
🏢 Office & Workplace
Maintain optimal work conditions, compliance monitoring, productivity improvement
🏭 Industrial Safety
Track hazardous gases, worker safety alerts, regulatory compliance documentation
🏥 Healthcare Facilities
Patient room monitoring, infection control, air purification system optimization
🎓 Educational Institutions
Classroom air quality, laboratory safety, environmental science projects
🌍 Environmental Research
Weather stations, pollution studies, community air quality mapping

## Slide 8
Technical Specifications
Machine Learning Model: Ensemble (RF + GBM + SVR + Ridge) (81.66% R² accuracy)
Feature Engineering: 23 features from 3 base sensors (Temperature, humidity, AQI)
Prediction Speed: < 50ms per reading (Real-time processing)
Dashboard Performance: < 2 seconds load time (Auto-refresh: 5 seconds)
API Rate Limiting: 10-100 requests/minute (DDoS protection)
Data Storage: SQLite with unlimited retention (Automated daily backups)
Concurrent Users: 50+ simultaneous users (Session management)
Uptime: 99%+ availability (Production-ready)

## Slide 9
System Benefits
✓ Cost-Effective
Affordable hardware ($30-50), open-source software, no subscription fees
✓ Easy Deployment
Plug-and-play sensors, simple WiFi setup, web-based interface
✓ Scalability
Support for multiple devices, multi-user access, expandable features
✓ Data-Driven Insights
Historical trends, predictive analytics, actionable recommendations
✓ Proactive Alerts
Early warning system, prevent health issues, automated notifications
✓ Maintenance-Free
Automated backups, self-healing database, minimal manual intervention
✓ Privacy-Focused
Local data storage, no cloud dependency, user-controlled access

## Slide 10
Dashboard Features
📊 Dashboard Page
  • Real-time AQI display with color-coded status
  • 4 stat cards: Total devices, readings, alerts, avg AQI
  • 6-hour forecast chart with trend visualization
🔌 Devices Page
  • Register and manage multiple IoT devices
  • Real-time online/offline status indicators
  • Last seen timestamp for each device
📈 History Page
  • Historical data table with filtering options
  • Date range selector and device filter
  • Sortable columns for easy analysis
⚠️ Alerts Page
  • Alert history with severity levels
  • Acknowledgment system to mark alerts as reviewed
  • Filter by device and alert type
📥 Export Page
  • Download data in CSV format
  • Date range and device selection
  • One-click export functionality
⚙️ Settings Page
  • Configure AQI thresholds
  • Email notification settings
  • Alert cooldown periods
🛡️ Admin Panel
  • System statistics and health monitoring
  • Database backup and restore
  • Data cleanup and optimization

## Slide 11
Future Enhancements
🌐 Cloud Integration: AWS/Azure deployment for global access
📱 Mobile Application: Native iOS/Android apps with push notifications
🤖 Advanced AI Models: Deep learning for improved prediction accuracy
🔗 IoT Platform Integration: ThingSpeak, Blynk, MQTT support
📍 GPS Location Tracking: Multi-location monitoring and mapping
🎯 Air Purifier Control: Automated control of air purification systems
📊 Advanced Analytics: Machine learning insights and recommendations
🔊 Voice Assistants: Alexa, Google Home integration
📧 SMS Notifications: Real-time alerts via SMS
🌡️ Additional Sensors: CO2, PM2.5, PM10, VOC sensors

## Slide 12
Conclusion
✓ Comprehensive IoT solution for air quality monitoring
✓ 81.66% accurate machine learning predictions
✓ User-friendly web dashboard with real-time updates
✓ Production-ready with enterprise features
✓ Scalable, cost-effective, and easy to deploy
✓ Ideal for homes, offices, industries, and research

## Slide 13
Thank You!